| Bil | Perkara | Unit | Kuantiti | Kadar | Harga |
| --- | --- | --- | --- | --- | --- |
| 1.0 | PRELIMINARIES |  |  |  |  |
| 1.1 | Provide Insurance of the Works, Public Liability Insurance, SOCSO/Workmen Compensation Insurance and other related issues. | L/Sum | L/Sum |  |  |
| 1.2 | Holding of labor, machinery and transportation to the site of execution of work including site cleaning and waste disposal. | L/Sum | L/Sum |  |  |
| 1.3 | To dismantle, assemble, deliver and unload old and damaged parts to BPME JPS Selangor or JPS Petaling as accordance to SO instruction. | L/Sum | L/Sum |  |  |
| 1.4 | To provide report of work done before, during and after completion (Soft Copy & Hard Copy) | Set | 3 |  |  |
| 2.0 | SCOPE OF WORKS |  |  |  |  |
| 2.1 | The contractor shall supply & install Side Rubber Seal, Rubber Pad, C Channel and Rubber Seal Flat Bar complete with other related accessories as in accordance to the site. | Set | 8 |  |  |
| 2.2 | The contractor shall supply & install Hardwood Bottom Seal complete with other related accessories as in accordance to the site. | Set | 2 |  |  |
| 2.3 | The contractor shall supply & install Cap Roller complete with other related accessories as in accordance to the site. | Set | 2 |  |  |
| 2.4 | The contractor shall supply & install Stainless Steel Bolt & Nut (m12x50mm) complete with other related accessories as in accordance to the site. | Nos | 640 |  |  |
| 2.5 | The contractor shall supply & install Wire Rope size 16mm, Bulldog Clip and Turn Buckle complete with accessories as in accordance to the site. | Set | 4 |  |  |
| Bil | Perkara | Unit | Kuantiti | Kadar | Harga |
| 2.6 | The contractor shall supply & install Greasing Pipe complete with accessories as in accordance to the site. | Set | 4 |  |  |
| 2.7 | The contractor shall maintain and repair Cast Iron Roller and other related accessories as in accordance to the site | Set | 12 |  |  |
| 2.8 | The contractor shall maintain and repair Gearbox "AKPA 2A" such as change oil gear, oil seal, Ball Bearing and other related equipment until the gearbox in good condition or can operate properly | Set | 2 |  |  |
| 2.9 | The contractor shall fabricate and install of new Counter Weight complete with other related accessories as in accordance to the site | Set | 1 |  |  |
| 2.10 | The contractor shall supply & install Motor Electric 3 Phase complete with Worm Gear and Out Put Shaft as below:- Rating - 2.2kW Voltage - 415V Frequency - 50hz RPM – 1432 Protection – IP55 Ratio - 1:20 | Set | 2 |  |  |
| 2.11 | The contractor shall supply & install 3 Phase TNB Meter Box complete with wiring and electrical components relevant. | Set | 1 |  |  |
| 2.12 | The contractor shall supply & install Electrical Control Panel complete with wiring IP65 Panel Box, Contractor, MCCB, Overload Relay, ELCB, double protection rubber door c/w control buttons, indicatorlamps, power supply, terminal block ventilation fan and electrical components relevant including the electrical drawing. | Set | 1 |  |  |
| 2.13 | The contractor shall supply and install 2.5mm x 12 core Armoured Cable to connect main panel to the actuator (control cable) motors including Hot Dip Trunking, Steel Band, Bracket Holder and other related components. | Mtr | 15 |  |  |
| Bil | Perkara | Unit | Kuantiti | Kadar | Harga |
| 2.14 | The contractor shall supply and install 4mm x 4 core Armoured Cable to connect main panel to the actuator (power cable) motors including Hot Dip Trunking, Steel Band, Bracket Holder and other related components. | Mtr | 15 |  |  |
| 2.15 | The contractor shall supply and install 4mm x 4 core Armoured Cable to connect TNB panel to the main panel including Hot Dip Trunking, Steel Band, Bracket Holder and other related components. | Mtr | 20 |  |  |
| 2.16 | The contractor shall supply & install Lightning Arrestor System using passive type (copper), copper tape and GI pipe including the Earthing System. Reading the of the lightning and earthing system testing shall not less than 5ohm. Contractor must provide related test report to JPS. | Set | 1 |  |  |
| 2.17 | The contractor shall supply & install Limit Switch complete with the wiring using 1.5mm x 2 core Armoured Cable to the main panel includes Hot Dip Trunking, Steel Band and Bracket. | Set | 2 |  |  |
| 2.18 | The contractor shall supply and install 5 set LED Floodlight and 3 set Bulkhead Lamp complete with wiring, 24-hour timer, on/off switch and cover with G.I conduit. | L/Sum | L/Sum |  |  |
| 2.19 | The contractor shall supply and install of water level Stick Gauge for up stream and down stream position on concrete wall including all related works for stick gauges leveling measurements. | Set | 2 |  |  |
| 2.20 | The contractor shall design, fabricate and install of new Safety Grille using expanded wire mesh with 3mm thickness around the tidal gate control platform complete with a locked gate and maintenance door. | Mtr | 25 |  |  |
| 2.21 | The contractor shall design, fabricate and install of new Safety Fencing using Anti Climb Anti Cut fence with 4mm diameter (2.1m Height x 2.4m Width) and 2.8m rectangular pole around the tidal gate control complete with bottom end embedded in concrete kerb and one panel locked gate. | Mtr | 25 |  |  |
| Bil | Perkara | Unit | Kuantiti | Kadar | Harga |
| 2.22 | The contractor shall design, fabricate and install of new weatherstrip Safety Staircase to replace the existing spiral staircase. Material specifications :- Pole – Galvanise Iron (G.I) Reinforcement – Mildsteel C Channel Barrier – Iron Galvanise Security Grille – Mildsteel Plate Bar The Frame Rung – Mildsteel Angle Iron Stairs - Fiberglass | Set | 1 |  |  |
| 2.23 | The contractor shall supply and install of new roofing using Metal Deck with minimum 3mm thickness c/w structure and other accessories to replace the existing roofing. | Mtr2 | 30 |  |  |
| 2.24 | The contractor shall Painting the whole Tidal Gate including main body structure, counter weight, stairs, hand railing, gear box, torque shaft, coupling and related accessories. (scrap the original paint) *The colour for painting works must be approved by the SO | L/Sum | L/Sum |  |  |
| 2.25 | The contractor shall supply and install of floor mat on the platform using ‘rubber/PVC mat’ type as an electrical insulation for safety in accordance to the specification set by project supervisor. | Mtr2 | 20 |  |  |
| 3.0 | OTHERS WORK |  |  |  |  |
| 3.1 | Testing and Comissioning (T&C) | L/Sum | L/Sum |  |  |
| 3.2 | ……………………………………………………………… ……………………………………………………………… ……………………………………………………………… |  |  |  |  |
|  | CARRIED TO COLLECTION |  |  |  |  |